## Slide 1
PROJECT DETAILS |  |  |  |  |  |  |  |  | 
NAME: 3-Bedroom Detached House Show Home |  |  |  | SITE ADDRESS: <site address> |  |  |  | CLIENT NAME: <client name> | 
CONTRACTOR DETAILS |  |  |  | 
NAME: <contractor’s name> | ADDRESS: <contractor’s address > | PHONE |  | E-MAIL: <contractor’s e-mail>
 |  | office: <###> | mobile: <###> | 
GENERAL INSTRUCTIONS and PREPATORY NOTES | 
1/ | Please review this specification, the reference drawings and schedules and contact me as soon as possible with any issues or questions.
2/ | This specification has separate sections for each of the partitions to be installed: Section 2 for the partition designated for the Downstairs Bathroom (Ground Floor), and Section 3 for the partition designated for the Shower Room (First Floor).
3/ | Important scheduling note for coordination with the flooring contractors: Both partitions must be installed after the vinyl floors in both bathrooms have been installed.
4/ | Please carry out all work with appropriate care taken so that no damage is inflicted on the newly installed floors.
5/ | No substitutions are to be made unless agreed upon ahead of time.
6/ | The specific manufacturer’s instructions are to be followed in each case.
7/ | As much as possible, please leave the work areas in a tidy fashion at the end of each day. All rubbish is to be promptly removed from the site.
MAIN DETAILS

## Slide 2
PRODUCT DETAILS |  |  |  |  |  |  |  | 
Ref ID within room | TYPE | BRAND / SUPPLIER | NAME | CODE / REF | COLOUR | DIMS INFO (mm) | REFERENCE DRAWING | INSTALLATION NOTES and WWW LINKS
4 | Partition | 3form | Varia Ecoresin /Organics / Criss Cross | Installation Solution Code for Top Support Suspended Partition: 200.25.01 | White, brown | Gauge: 12.7 (1/2”) Custom sized: 900W x 2298.4H 101.6 (4”) is the allowance for fitting the top and bottom hardware channels that will hold the partition in place [Panel height(2298.4) = Opening height(2400) – 4”]. | (D5) Painter/Decorator/Installer - Ground Floor (See label on drawing) | Product info: http://www.3-form.com/materials/varia_ecoresin/organics/criss_cross/#4 To be installed using the Top Support system with surface mounted (to floor and ceiling) hardware channels. For more info: http://www.3-form.com/ready_to_go/partitions/200.25/ Detailed installation instructions: http://www.3-form.com/downloads/3form_harspec_topsupport_Man-026_Rev006.pdf Please see this manual for instruction on how to trim the panel if any height adjustment is necessary: http://www.3-form.com/downloads/3form_Varia_Fabrication_Manual_REV007.pdf
DOWNSTAIRS BATHROOM

## Slide 3
PRODUCT DETAILS |  |  |  |  |  |  |  | 
Ref ID within room | TYPE | BRAND / SUPPLIER | NAME | CODE / REF | COLOUR | DIMS INFO (mm) | REFERENCE DRAWING | INSTALLATION NOTES and WWW LINKS
4 | Partition | 3form | Varia Ecoresin /Wood / Zebrano Chevron | Installation Solution Code for Top Support Suspended Partition: 200.25.01 | Brown | Gauge: 12.7 (1/2”) Custom sized: 900W x 2298.4H 101.6 (4”) is the allowance for fitting the top and bottom hardware channels that will hold the partition in place [Panel height(2298.4) = Opening height(2400) – 4”]. | (D6) Painter/Decorator/Installer – First Floor (See label on drawing) | Product info: http://www.3-form.com/materials/varia_ecoresin/wood/zebrano_chevron/ To be installed using the Top Support system with surface mounted (to floor and ceiling) hardware channels. For more info: http://www.3-form.com/ready_to_go/partitions/200.25/ Detailed installation instructions: http://www.3-form.com/downloads/3form_harspec_topsupport_Man-026_Rev006.pdf Please see this manual for instruction on how to trim the panel if any height adjustment is necessary: http://www.3-form.com/downloads/3form_Varia_Fabrication_Manual_REV007.pdf
SHOWER ROOM